SECTION 101100 - VISUAL DISPLAY UNITS

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 01 Specification Sections, apply to this Section.

SUMMARY

Section Includes:

Marker Boards

Related Requirements:

Section 092216 Non-Structural Metal Framing.

ACTION SUBMITTALS

Product Data: For each type of product.

Include construction details, material descriptions, dimensions of individual components and profiles, finishes, and accessories for visual display units.

Shop Drawings: For visual display units.

Include plans, elevations, sections, details, and attachment to other work.

Show locations of panel joints. Show locations of field-assembled joints for factory-fabricated units too large to ship in one piece.

Include sections of typical trim members.

CLOSEOUT SUBMITTALS

Maintenance Data: For visual display units to include in maintenance manuals.

WARRANTY

Special Warranty for Porcelain-Enamel Face Sheets: Manufacturer agrees to repair or replace porcelain-enamel face sheets that fail in materials or workmanship within specified warranty period.

Warranty Period: 5 years from date of Substantial Completion.

PRODUCTS

MANUFACTURERS

Visual Display Boards

Claridge Products and Equipment, Inc.

Platinum Visual Systems

US Markerboard

Nelson Adams NACO

Markerboards

Dual track markerboard with pen tray and track strip at top

Size: As indicated on drawings

Frame Finish: Anodized natural

Materials: Porcelain-enamel-faced steel sheet: ASTM A424/A424M, Type 1, Commercial Steel with fired on vitreous finish.

Color: White

Aluminum Frames and Trim: Fabricated from not less than 0.062-inch- (1.57-mm-) thick, extruded aluminum; standard size and shape.

GENERAL FINISH REQUIREMENTS

Comply with NAAMM/NOMMA 500 for recommendations for applying and designating finishes.

Protect mechanical finishes on exposed surfaces from damage by applying a strippable, temporary protective covering before shipping.

Appearance of Finished Work: Noticeable variations in same piece are unacceptable. Variations in appearance of adjoining components are acceptable if they are within the range of approved Samples and are assembled or installed to minimize contrast.

EXECUTION

EXAMINATION

Examine substrates and conditions, with Installer present, for compliance with requirements for installation tolerances, surface conditions of wall, and other conditions affecting performance of the Work.

Examine walls and partitions for proper preparation and backing for visual display units.

Proceed with installation only after unsatisfactory conditions have been corrected.

PREPARATION

Comply with manufacturer's written instructions for surface preparation.

Clean substrates of substances, such as dirt, mold, and mildew, that could impair the performance of and affect the smooth, finished surfaces of visual display boards.

Prepare surfaces to achieve a smooth, dry, clean surface free of flaking, unsound coatings, cracks, defects, projections, depressions, and substances that will impair bond between visual display units and wall surfaces.

INSTALLATION

General: Install visual display surfaces in locations and at mounting heights indicated on Drawings, or if not indicated, at heights indicated below. Keep perimeter lines straight, level, and plumb. Provide grounds, clips, backing materials, adhesives, brackets, anchors, trim, and accessories necessary for complete installation.

Visual Display Board Assembly Mounting Heights: Install visual display units at mounting heights indicated on Drawings, or if not indicated, at heights indicated below.

Mounting Height :  30 inches (mm) above finished floor to top of chalktray.

CLEANING AND PROTECTION

Clean visual display units in accordance with manufacturer's written instructions. Attach one removable cleaning instructions label to visual display unit in each room.

Touch up factory-applied finishes to restore damaged or soiled areas.

Cover and protect visual display units after installation and cleaning.

END OF SECTION 101100