August 3, 2020

Project:		El Paso County

Pikes Peak Work Force Center and Health Center Remodel

1675 W. Garden of the Gods Road

Colorado Springs, CO

Architectural Addendum:

Revisions- Delta 1,  7-27-20

- Remove existing chair rail in Waiting 1053

  - Ref: A1.1, Demo Floor Plan – Health Center

- Additional information on fire alarm locations, removals and relocations.

  - Ref: A1.1, all demo and construction plans

- New gypsum board in Classroom 1125

  - Ref: A1.1, Constr Floor Plan – Room 1121 + 1126

- New wall with door in Hallway 1141

  - Ref: CS, Egress Plan

  - Ref:A1.1, Construction Floor Plan – Rm 1142 + 1126

  - Ref: A2.0, Door Schedule

- Additional information on floor finishes.

  - Ref: A1.1, Construction Floor Plan

  - Ref: A2.20, Room Finish Schedule, Finish Schedule

  - See attached for LVT-1 spec.

SECTION 09 65 00 RESILIENT FLOORING

PART 1: GENERAL

1.01 SUMMARY

- Section includes:

  - Luxury Vinyl Tile (LVT).

1.02 SUBMITTALS

- Submit the following in accordance with Section 01 33 00:

  - Submit full line of color samples for materials to be furnished for Architect's review and selection.

  - Provide manufacturer's recommended maintenance data and instructions prior to completion of work.

  - Specified warranties from manufacturer. Submit per Section 01 78 23.

1.03 CONCRETE MOISTURE AND ADHESION

- For new concrete slabs on grade, this project is utilizing a moisture vapor reduction admixture (MVRA) as specified in Section 03 30 00.

  - The MVRA manufacturer will perform all moisture testing of new slabs on grade. No further field slab moisture or pH testing shall be required by the flooring installer. Probe type moisture tests will not provide accurate results with concrete that has MVRA admixture, as the moisture remains irremovable and suspended within the slab.

  - The flooring installer is to perform a field bond test with the specified flooring products and the flooring manufacturer’s recommended adhesive for non-porous substrates, with the MVRA manufacturer’s representative present. The bond test shall be performed to adhesive manufacturer’s guidelines and ASTM F710.

  - At completion of testing and prior to the installation of any flooring, the MVRA manufacturer will issue the following warranties/guarantees:

    - Life of Concrete Warranty that states the MVRA products ability to stop moisture vapor emission from the concrete itself for the life of the concrete.

      - Up to 25 pounds of moisture per ASTM F1869 or 100% RH per ASTM F2170.

    - Adhesion Guarantee stating the MVRA manufacturer will guarantee and warrant that the materials bond tested will adequately bond directly to the MVRA dosed concrete.

1.04 FLOOR FLATNESS

- For new concrete slabs on grade and elevated structural slabs/topping as specified in Section 03 30 00 floor flatness is specified per ACI 117 as follows:

  - F (F) Flat tolerance with an overall value of 35 and a minimum localized value of 21.

  - F (L) Flat tolerance with an overall value of 25 and a minimum localized value of 15.

3. Measured by a manual straightedge method a “flat” floor surface classification, maximum gap for 90% compliance, samples not to exceed ¼” and for 100% compliance, samples not to exceed 3/8”.

B. The flooring contractor will be responsible to provide the necessary means (i.e., grinding/leveling) for additional leveling as required by the flooring manufacturer.

1.05 PRODUCT DELIVERY, STORAGE AND HANDLING

- Deliver materials to project site in manufacturer's original, unopened containers with labels indicating brand names, colors and patterns, and quality designations legible and intact.

- Do not open containers or remove markings until materials are inspected and accepted.

- Store and protect accepted materials in accordance with manufacturer's directions and recommendations.

- Unless otherwise directed, store materials in original containers at not less than 70° F. for not less than 24 hours immediately before installation.

1.06 ENVIRONMENTAL REQUIREMENTS

- Maintain temperature in space to receive tile between 70° F. and 90° F. for not less than 48 hours before and 48 hours after installation.

- Maintain minimum temperature of 65° F. thereafter.

1.07 WARRANTY

- Luxury Vinyl Tile (LVT):

  - 10 year manufacturing and installation integrity.

PART 2: PRODUCTS

2.01 APPROVED MANUFACTURERS

- Manufacturers listed in this specification are approved under the following conditions:

  - A manufacturer listed in both the specification and the Interior Material Finish/Color Schedule, on Architectural Drawings is not required to submit a pre-bid approval.

  - Manufacturers listed in this specification, but not in the Interior Material Finish/Color Schedule, on Architectural Drawings shall submit color samples for pre-bid approval by addendum. Refer to Section 01 25 00.

  - When no colors are listed in the Interior Material Finish/Color Schedule, on Architectural Drawings, any manufacturer listed in this specification are not required to submit a pre-bid approval.

2.02 LUXURY VINYL TILE (LVT)

- Product specified are manufactured by Armstrong World Industries. Other manufacturers that meet the requirements of this specification are acceptable.

  - Resilient Flooring consisting of clear, unfilled, polyurethane-coated, 0.020 inch thick wear layer composed of polyvinyl chloride resins, plasticizers, stabilizers, and processing aids over a printed film on an intermediate layer over a filled vinyl backing. “Standard Specification for Solid Vinyl Tile”, Class III, Type B, Embossed Surface.

  - Standards: Meet or exceed requirements of ASTM F 1700.

09 65 00-2 Resilient Flooring

- Gauge and Size: 1/8 inch, 18 inch by 18 inch and 6 inch by 48 inch.

- Flammability: Provide materials with 0.45 CRF (critical radiant flux) or higher when tested in accordance with ASTM E 648, Flooring Radiant Panel Test.

- Smoke Density: Provide materials with smoke density of less than 450 when tested in accordance with ASTM E662.

- Static Load: Provide materials with static load limit of 250 psi or higher.

- Colors: See Interior Material Finish/Color Schedule on Architectural Drawings.

- Patterns: as indicated on Drawings.

- Adhesives:

  - S-288 Premium Commercial Vinyl Sheet Flooring Adhesive, water based resin, less than 14 g/l, VOC adhesive for above grade.

  - S-543 Premium Plus Commercial Vinyl Sheet Floor Adhesive, water based synthetic polyer, zero regulated VOC, high-moisture area adhesive for slab on grade installation.

2.03 VINYL OR RUBBER BASE

- Manufacturer: Match Existing. Products by Johnsonite, VPI, Armstrong, Burke, Roppe, Tarkett are acceptable.

- Base: 1/8" thick x 4" high, solid vinyl. Straight base at carpet, coved base at other surfaces, where applicable.

2.04 ACCESSORIES

- Adhesives, Other Application Material: As recommended specifically by flooring manufacturer.

- Subfloor Filler: Hydraulic/Portland cement based material designed for providing thin solid surface for leveling and for minor ramping of subsurface to adjacent floor finishes.

  - Use material capable of being applied and feathered out to adjacent floor without spalling.

- Crack and Joint Treatment: ARDEX ARDIFIX or equal (dormant cracks), two part, low viscosity rigid polyurethane and/or ARDEX ARDISEAL or equal (moving joints and cracks), rapid plus fast setting semi-rigid joint sealant.

- Substrate Prep: ARDEX MRP or equal, moisture resistant patch.

- Self Leveling Topping (Underlayment): ARDEX K15 or equal, Portland Cement-based, self leveling topping.

- Transition strips, cap strips: Mercer. Color: See Interior Material Finish/Color Schedule, on Architectural Drawings.

  - Transition/Reducer strips must be provided at all floor type transitions occurring within a room not at a door. Refer to accessories manufacturer for appropriate transition/reducer profile required for specified floor types.

- Non-slip strips: 3M Company.

- Finish products for VCT as manufactured by Johnson Wax. Cleaner: Forward; Sealer: Technique; Wax: Vectra.

2.05 EXTRA STOCK

A. Furnish 1% of each type/color of flooring, trim used in this project to Owner as maintenance stock.

09 65 00-3 Resilient Flooring

No. 205029 09 65 00-4 Resilient Flooring

PART 3: EXECUTION

3.01 PREPARATION

- Surfaces to receive resilient finishes: Dry, clean, smooth. Fill defects or grind smooth as required. Sand subfloors to remove mortar, paint, other surface irregularities.

- Buff out the concrete curing compound with a scouring pad on a buffer or other recommended procedure prior to installing adhesives for flooring.

- Correct adverse conditions of any type before starting any flooring installation.

- Slab preparation and moisture mitigation installation to be per manufacturer’s instructions.

- Where filling, patching, leveling is required of thickness exceeding 1/8" apply latex type underlayment in two or more applications. Apply compound in accordance with Manufacturer's printed instructions. Achieve a substrate that is flat to within 1/8” in 10’.

  - On remodeling projects, assume 33% of area will require filling, patching or leveling.

- Beginning of installation means installer has accepted substrate as acceptable.

- Install flooring only after finishing operation has been completed and permanent heating system is in operation. Moisture content of concrete slabs, building air temperature and relative humidity must be within limits recommended by flooring manufacturer.

- Terminate resilient flooring at centerline of door openings where adjacent floor finish is dissimilar.

3.02 LUXURY VINYL TILE (LVT)

A. Install flooring in strict accordance with the latest edition of “Armstrong Guaranteed Installation System, F-5061”.

3.03 ACCESSORIES

- Place resilient reducer strips tightly butted to resilient flooring and secure with adhesive. Provide edging strips or cap strips at all unprotected edges of flooring.

- Apply coved base at resilient floors and straight base at carpeted floors.

3.04 DEMONSTRATION

A.

Engage factory-authorized representatives to train Owner’s maintenance personnel on proper waxing and cleaning procedures for each floor product. Refer to Section 01 79 00 Demonstration and Training.

END OF SECTION 09 65 00